## Slide 2: The Life Alerting Safety Cane
By Derek Feng and Jerry Shen

## Slide 3: Defining the Problem
In 2016
  ~591 deaths from falls for every 100,000 people 95 and older
  ~42 for every 100,000 people ages 75 to 79
  Deaths from falls among U.S. adults aged 75 or older rose from 8,613 in 2000 to 25,189
  https://www.reuters.com/article/us-health-elderly-falls/more-elderly-americans-dying-from-falls-idUSKCN1T5213

## Slide 4: Proposed Solution
IoT cane that detects and alerts when there’s a fall
If there’s a fall, send an SMS text to designated contact
To prevent false positives, user can press a button to send an SMS text saying that it’s a false alarm

## Slide 5: Implementation
Arduino (slave)
  Accelerometer to detect falls
  Button to send the false alarm SMS
  LED light to indicate when the cane detected a fall
  GPS to track the latest movement of the user
Raspberry Pi (master)
  Receives the info from Arduino
  Connects to WiFi
  Sends the GPS data to cloud service (ThingSpeak)
  If fall/button press detected from Arduino, send SMS (Twilio)

## Slide 6: ThingSpeak Channel Data

## Slide 8
Fall Detected
False Alarm

## Slide 9: Challenges and Solution
3D print a whole cane and an enclosure for the Arduino + Pi + sensors
  Bought a cane and made enclosure out of cardboard
ESP8266 troubles
  Managed to setup as webserver, but not sure how to go on from there
  Used a Raspberry Pi to connect to Arduino
GPS requires direct line of sight to the sky
  Recorded the demo